## Slide 1: Asbestos Awareness Training
Surry Insurance Loss Prevention Services

## Slide 2: Course Outline
The following topics will be covered:
Types & properties of asbestos
Uses of asbestos
Health effects of asbestos
General asbestos rule requirements

## Slide 3
Serpentine Rock (Chrysotile) - California State Rock
What is Asbestos?

## Slide 4
Close-up of Asbestos Fibers

## Slide 5: Common Types of Asbestos
Chrysotile – most common
“White Asbestos”
Amosite
“Brown Asbestos”
Crocidolite – least used
“Blue Asbestos”
Chrysotile asbestos mine in Canada

## Slide 6: Other types of asbestos -
  Tremolite (Libby vermiculite mine-actually winchite-richterite)
Actinolite
Anthophyllite

## Slide 7: Vermiculite
Vermiculite ore
“Popped” Vermiculite
Vermiculite insulation in attics

## Slide 8
Libby Vermiculite Mine
Photo of operating Libby mine
Libby Mine site today
Zonolite insulation

## Slide 9: Uses of Asbestos
Asbestos = “inextinguishable”
Egyptians; Greeks & Romans
Middle Ages
Industrial Revolution
Twentieth century –
*World War II + next 30 years

## Slide 10: Properties of Asbestos
Asbestos ore
Good tensile strength
Flexibility
Heat resistance
Electrical resistance
Good insulation
Chemical resistance
Naturally occurring fibrous minerals

## Slide 11: Some Asbestos-Containing Materials*
(This list does not include every product/material that may contain asbestos. It is intended as a general guide to show which types of materials may contain asbestos.)
Cement Pipes
Cement Wallboard
Cement Siding
Asphalt Floor Tile
Vinyl Floor Tile
Vinyl Sheet Flooring
Flooring Backing
Acoustical Plaster
Decorative Plaster
Textured Paints/Coatings
Ceiling Tiles and Lay-in Panels
Spray-Applied Insulation
Blown-in Insulation
Fireproofing Materials
Taping Compounds (thermal)
High Temperature Gaskets
Laboratory Hoods/Table Tops
Laboratory Gloves
Fire Blankets
Fire Curtains
* Source: EPA

## Slide 12: Some Asbestos-Containing Materials
(Continued)
Chalkboards
Roofing Shingles
Roofing Felt
Base Flashing
Thermal Paper Products
Fire Doors
Caulking/Putties
Adhesives
Wallboard
Joint Compounds
Vinyl Wall Coverings
Spackling Compounds
Elevator Equipment Panels
Elevator Brake Shoes
HVAC Duct Insulation
Boiler Insulation
Ductwork Flexible Fabric Connections
Cooling Towers
Pipe Insulation (corrugated air-cell, block, etc.)
Heating and Electrical Ducts
Electrical Panel Partitions
Electric Wiring Insulation

## Slide 13: Asbestos is an Inhalation Hazard
Respirable fibers are inhaled and deposited in the lungs
Body’s defense mechanisms cannot break down the fibers
Fibers cause damage to respiratory system
Airborne asbestos fibers inhaled deep into the lung can cause damage.
Damage occurs in the alveoli

## Slide 14: Asbestos-related diseases
Asbestos can cause disabling respiratory disease and various types of cancers if the fibers are inhaled.
- Asbestosis
- Lung Cancer
- Mesothelioma
- Other cancers

## Slide 15: Smoking and Asbestos
70 per 100,000 lung cancer deaths in general population
Lung Cancer Risks
5x higher risk than general population
10x higher risk
50x to 90x higher risk

## Slide 16: Asbestosis Example
Joe Darabant, 1949.
Covered with chrysotile asbestos fibers. Worked for 30+ years at the Johns-Manville Plant in New Jersey, cutting asbestos shingles and making asbestos block and pipe-covering materials.
Joe, 1989.
Forced to retire in 1974 at age 50 from poor health; he died from asbestosis in 1990 at age 66.
Photos ©RAVANESI@2000

## Slide 17: Current worker exposure to asbestos
In general industry, exposure can occur in:
  manufacture of asbestos products
  automotive brake and clutch repair
  housekeeping and custodial work
An estimated 1.3 million workers are exposed in U.S. today.
In the construction industry, removal renovation and demolition have heaviest exposures.

## Slide 18
Where could you be exposed to asbestos?
Asbestos had a variety of uses in building construction completed before 1981. You could be exposed to asbestos during inspection of the following activities in these older buildings:
Asbestos removal projects
Building insulation maintenance or repair
Heating and air conditioning maintenance and repair
Insulated piping maintenance repair
Floor tile or flooring replacement or repair
Roofing or siding replacement or repair
Wallboard(sheetrock) or wall plaster replacement or repair
“Popcorn ceiling” replacement or repair
Janitorial or maintenance work done in pre-1981 buildings
Building demolition

## Slide 19: Brief history of U.S. asbestos regulation
British physicians noted that asbestos workers developed lung disease in early 1900’s.
Lung disease noted in American asbestos workers in 1930’s. Some companies actively suppressed this information.
Dr. Irving Selikoff at Mt. Sinai Hospital in New York began studying asbestos workers in 1960’s.
His published research led OSHA to adopt specific standard on asbestos in early 1970’s.
OSHA lowered the PEL for asbestos several times through 1970’s, 1980’s and 1990’s.

## Slide 20: Thermal System Insulation (TSI)
Damaged insulation on control valve
Air cell pipes
Asbestos insulation on outdoor pipe

## Slide 21
Thermal system insulation close-up

## Slide 22
Asbestos air cell insulation (pipe insulation)
Visible asbestos fibers

## Slide 23
“Mag” Pipe Insulation

## Slide 24: Asbestos Duct Tape

## Slide 25
More Thermal System Insulation
Asbestos insulated furnace
Asbestos insulated boiler

## Slide 26: Asbestos gaskets, rope and packing – may be round, flat or impregnated with waterproof sealant
Asbestos fabric in HVAC system
Damaged asbestos gasket
Asbestos rope

## Slide 27
Asbestos Ceiling Tile
Usually in 1’ by 1’ or 2’ by 4’ sizes
Tile close-up

## Slide 28
Asbestos shingle siding

## Slide 29: Asbestos Roofing Material

## Slide 30
Vinyl asbestos and asphalt asbestos flooring

## Slide 31: Asbestos Sheet Vinyl
Uncontrolled sheet vinyl removal

## Slide 32: Surfacing Material
Acoustical material
Sprayed-on surfacing material

## Slide 33
Spray-on insulation containing asbestos

## Slide 34
Asbestos fireproofing in ceiling and above dropped ceiling

## Slide 35: Popcorn Ceiling Material
damaged and friable popcorn ceiling material
Uncontrolled popcorn ceiling removal job
###

## Slide 36
Chimney flue packing (mud) containing asbestos

## Slide 37: Asbestos Mill Board

## Slide 38
Asbestos Brake Pads & Discs

## Slide 39: Asbestos in joint compound and plaster

## Slide 40: How do asbestos fibers get in the air?
Physical disturbance of asbestos-containing materials (ACM) suspends fibers in the air.
Friable: can be easily crumbled or crushed by hand, releasing fibers into the air
Very small fibers stay in the air for long periods
Damaged or deteriorated ACM increases friability
Asbestos is most hazardous when it is FRIABLE.

## Slide 41: How do asbestos fibers get in the air?
Mechanical action on ACM (cutting, sawing, grinding, sanding, drilling, buffing, etc.)
Disturbing/breaking ceiling tiles
Removing/replacing insulation
Disturbing sprayed-on asbestos
Asbestos abatement projects
Un-surveyed construction projects on older buildings
Some typical activities and situations that can result in asbestos exposure:
Debris from disturbance of “popcorn” ceiling

## Slide 42: “ACM” and “PACM”
Surfacing materials
Thermal System Insulation
Flooring
Installed prior to 1981
Must be handled as ACM unless proved otherwise
Presumed Asbestos Containing Material
Asbestos Containing Material
Any material containing more than 1% asbestos by weight.

## Slide 43: Communication of Hazards
Warning Signs
  for regulated areas
  visible before entering
Warning Labels
  attached to all products and their containers
AVOID BREATHING AIRBORNE ASBESTOS FIBERS

## Slide 44: Custodial/Light maintenance work
Some materials of concern:
  vinyl asbestos tile
  exposed piping
  exposed fireproofing
  popcorn ceiling
Activities:
  sweeping
  vacuuming
  cleaning
  changing lights
Housekeeping and building maintenance activities may expose workers to asbestos fibers if ACM/PACM is disturbed.
Damaged asbestos pipe insulation
Asbestos debris on floor

## Slide 45: Custodial/Light maintenance work
Disturb ACM when replacing light bulbs, etc.
Sand asbestos floor tiles or backing material
Pin or hang pictures, plants, or objects on walls or from ceilings covered with asbestos materials
DO NOT:
Dry dust or sweep surfaces, ceilings, walls, or floors

## Slide 46: Custodial/Light maintenance work
Wet mop floors
Use only a HEPA-filtered vacuum to clean up asbestos debris
DO:
Dust with a damp cloth

## Slide 47: Steve McQueen
McQueen developed a persistent cough in 1978. He gave up cigarettes and underwent antibiotic treatments without improvement. Shortness of breath grew more pronounced and on December 22, 1979, after filming The Hunter, a biopsy revealed pleural mesothelioma, a cancer associated with asbestos exposure for which there is no known cure.
A few months later, McQueen gave a medical interview in which he blamed his condition on asbestos exposure. McQueen believed that asbestos used in movie sound stage insulation and race-drivers' protective suits and helmets could have been involved, but he thought it more likely that his illness was a direct result of massive exposure while removing asbestos lagging from pipes aboard a troop ship while in the Marines.
50 years old when he died

## Slide 48: Areas of Asbestos – High School

## Slide 49: Areas of Asbestos – Middle School

## Slide 50: Buildings That DO NOT Contain Asbestos Materials
- Perquimans Central School
- Board of Education
- Transportation Department
- Maintenance Department
- Hertford Grammar (All ACM has been Abated 2021 – 2022 School Year)

## Slide 51
Thank you!